        NaviCar
2nd Year Internet of Things Project
Nathan Ferry
BEng(Hons) Software and Electronic Engineering
Scan here
for audio
Project Summary
Architecture Diagram
Website Data
The automotive industry has been attempting to implement the highest safety standard for decades, and the NaviCar shows that with self-driving technology, road deaths and accidents can be reduced even further with the absence of human error. The NaviCar is a self-autonomous vehicle that utilises many components to operate, such as:
Two SEN0017 line sensors to detect and follow a line.
Two DC motors to drive the chassis using an L293D motor driver with an ESP32 microcontroller.
A DHT11 to measure temperature and humidity and pass it to a website live. The temperature is also passed to the HC-SR04 ultrasonic sensor to calculate the NaviCar’s distance between itself and obstacles more accurately.
A Servo motor which is paired with, and rotates, an ultrasonic sensor for the sensor to read the value on the NaviCar’s left and right when turning and avoiding obstacles.
A GPS which passes the live location of the NaviCar to the website
With ThingSpeak, the NaviCar can put data onto the cloud and up on a website live. It can display the temperature and humidity live. A user can click the link to view the NaviCar’s current co-ordinates.
My website displays the live temperature and humidity on two graphs alongside the live GPS co-ordinates.
My website uses Flexbox for a responsive webpage design.
Sustainable Development Goals
The NaviCar
Goal 3: The NaviCar targets the U.N. goal target 3.6 which is to half the number of road deaths and accidents by 2030.
The NaviCar uses sensing technology to avoid collisions when moving forward while never deviating from a set path. The NaviCar uses 2 SEN0017s for path following.
Goal 11: Target 11.2 is to providing access to safe, affordable, accessible and sustainable transport systems as well as improve road safety for all.
The NaviCar’s ability to follow a predetermined path and sense upcoming collisions leads to improved road safety. The NaviCar can avoid possible collisions by braking and senses with the ultrasonic sensor.
Skills and Technologies\Hardware
Hardware & software debugging
Logical problem solving
Visual Studio Code
3D Modelling/printing
Arduino programming
HTML/CSS
IoT analytics with ThingSpeak
C/C++
DC Motors
GPS Ultimate V3
DHT11
SEN0017 line sensors
L293D motor driver
ESP32 microcontroller
HC-SR04 ultrasonic sensor
Servo motor